## Slide 1: Spectroscopic Reference Design Options
D. L. DePoy
Texas A&M University

## Slide 2: Notional DESpec unit spectrograph specs
550-1000nm coverage using DES 2Kx4K CCD
Roughly 4 pixels per resolution element (R~1760 at 775nm; 0.11 nm/pixel dispersion)
~4000 individually targetable fibres

## Slide 3: No metal has been cut (the cuts are not even designed!)
Could use 2 pixels per resolution element
  Resolution ~4000 rather than ~2000
Could “assign” some fibers to fixed geometry bundle
  For clusters or other “closely packed” targets
Could use “fiber bundle” IFUs instead of single fibers
  Rotation curves of galaxies or higher throughput

## Slide 4: Higher resolution
Need longer focal length camera
  Or finer grating
Better image quality from camera
  “line spread function” <30 microns
  However, typical galaxy velocity dispersions are ~150 km/sec
Could split beam into blue and red “arms”
  Cost would rise for spectrographs

## Slide 5: Fiber bundles
Could allocate some fibers to IFU
Murphy et al., 2008, SPIE 7018-104; Soukup et al., 2010, SPIE 7735-180
Kelz et al., 2006, SPIE 6273-121;
IFU output
IFU input

## Slide 6: Fixed fiber bundles
Closely packed targets may require many exposures
  Currently roughly 1 fiber per 2 arcminute diameter patch on the sky
  If target density is higher, will require multiple exposures
  Galaxy clusters may have 10-100 objects per arcminute

## Slide 7: Fixed fiber bundles
Could allocate fixed pattern to central field
  ~3 exposures for 100% coverage of area
  ~1600 fibers for 1 sq. arcminute
    Assumes 1.5 arcsec fiber
  ~8 additional spectrographs
Limit would be to carpet entire focal plane in fixed configuration
  ~17 million fibers
  70,000 spectrographs
  Project cost would be high

## Slide 8: Hybrid approach
Use small “IFUs” instead of single input fibers
  Each positioner has a bundle of N fibers
  N*size = field-of-view of each IFU
  e.g. ~15 arcsec field, 1.5 arcsec fibers
    ~50% fill factor
    Roughly 50 fibers per IFU
    Rotation curves for every galaxy larger than ~few arcsec
    Need ~50 times as many spectrographs
      ~750 spectrographs
      Already building 200 for HETDEX
  Other combinations possible of course

## Slide 9: Summary
Many options still open
Need to allow science goals to drive instrument choices
Should coordinate science ideas with changes in instrument design